## Slide 1: Control of an Electrically Powered Two-Spool Turbine Device Advanced Courses in Engineering 19 Jan 2017 rev. 1
Former Instructors:
Dave Gutz (rev 2017-1)
PICTURE

## Slide 2: Outline
Description of Project
Wind Turbine Primer
Modeling and Linearization
Lab

## Slide 3: Description of Project

## Slide 4
Regulator: Subsystem or independent device that determines and maintains the operating parameters of a system, usually within certain prescribed or preset limits. Read more: http://www.businessdictionary.com/definition/regulator.html
In control theory, a controller is a device, historically using mechanical, hydraulic, pneumatic or electronic techniques often in combination, but more recently in the form of a microprocessor or computer, which monitors and physically alters the operating conditions of a given dynamical system.[1] [2]Typical applications of controllers are to hold settings for temperature, pressure, flow or speed.
Open-loop control can be used in systems sufficiently well-characterized as to predict what outputs will necessarily achieve the desired states. For example, the rotational velocity of an electric motor may be well enough characterized for the supplied voltage to make feedback unnecessary.
The drawback of open-loop control is that it requires perfect knowledge of the system (i.e. one knows exactly what inputs to give in order to get the desired output), and it assumes there are no disturbances to the system.

## Slide 5: Wind Turbine Primer

## Slide 6: Wind Turbine Overview

## Slide 7: Wind Turbine Primer
, ,
where
= power available in the wind, W,
= power extracted by turbine, W,
= wind speed, m/s,
= air density, kg/m^3,
A = turbine flow area, m^2,
= turbine power extraction coefficient (0-1),
= angular speed of turbine, r/s = , and
= rotational speed of turbine, rpm.
Define another useful relationship:
http://www.nrel.gov/docs/fy12osti/52780.pdf
Santoso,S. and Singh, M. “Dynamic Models for Wind Turbines and Wind Power Plants,” National Renewable Energy Laboratory Publication, UT Austin, Austin, Texas, NREL/SR-5500-52780 October, 2011.
https://en.wikipedia.org/wiki/Variable_speed_wind_turbine

## Slide 8: Speed-Speed Relationship
The project operates the turbine unloaded in a freewheeling condition at =0. Here
=0 and
constant, where
= turbine tip speed ratio = ,
= wind speed, m/s, and
= turbine tip speed, m/s.
The gas generator that supplies the air flow, , will do so with cubic power and
square law thrust well known:
,
and
,
where
= gas generator speed, rpm,
A = cross-sectional area of wind field, m^2,
T = air thrust with stationary gas generator fan,
= air density, kg/m^3.
From this, three useful relationships emerge
,
, and
.
The turbine behaves like a screw in incompressible flow.

## Slide 9: Power Coefficient Characterized by Tip Speed Ratio
https://en.wikipedia.org/wiki/Variable_speed_wind_turbine
Slope is related to damping torque ( N )

## Slide 10
Get content from my white book
Get Cp curves from my personal OneNote
Assumption: neglect laminar flow Re effects

## Slide 11: Deriving Damping from Measured Time Constant
,
Where
= wind speed, m/s,
= air density, kg/m^3,
D = turbine tip diameter, m,
A = turbine flow area, m^2,
= turbine power extraction coefficient = 0 at freewheel condition,
= turbine tip speed ratio = ,
, chain rule
measurement for time constant.

## Slide 12: Measuring Damping to Calibrate the Model
,
where
= torsional time constant of air-damped turbine inertia, s,
and
J = turbine inertia, N-m/(rpm/s).
Therefore
= .
Then, since is invariant, is invariant and a model equation for may be derived from a measurement at one operating condition. In reality, it is necessary to verify this model so multiple measurements should be made and a regression fit performed for the best result.

## Slide 13: Summary of Turbine Dynamic Model
In summary:
, where
= wind speed, m/s, estimated from using device ratings.
= air density, kg/m^3,
D = turbine tip diameter, m,
A = turbine flow area, m^2,
= constant measured as described earlier
= turbine tip speed ratio = =constant.

## Slide 14: Practical Implementation of Turbine Dynamic Model
The turbine does not move until friction is overcome. This shifts the relationship between speed/airflow and time constant.
The shift may be approximated by
= -, where
= wind speed where turbine breaks free, m/s. This modified wind speed is then used in the previous equation.
Alternatively, if the relationships are derived using a speed shift instead,
Either method produces approximately accurate results, since the
Neither method is perfect, so in the end, an empirical curve as a function of turbine speed is used. The primary source of variation with that empirical approach is air property which could be dealt with at some future time using corrected parameters.

## Slide 15: ESC – Electronic Speed Control of Brushless DC Motor (BLDC)

## Slide 16: DC Motor Dynamic Model
http://www.profjrwhite.com/system_dynamics/sdyn/s6/s6fmathm/s6fmathm.html
Bandwidth > 30 Hz

## Slide 17: Modeling

## Slide 18: Moment of Inertia of Propeller

## Slide 19: Motor Constants – SI Units Assumptions
The main thing I want you to take away from this post is that when a motor rotates it generates a back-emf. That back-emf is proportional to the motor speed and the Kv constant tells you how they relate to each othe

## Slide 20
2040 Brushless Inrunner Motor 4800kv

## Slide 22: Landscape of Control System Analysis
Physical System
Non-Linear Ordinary Differential Equations
Linear Differential Equations
Block Diagram
Control
Models
Z-Transform
Embedded
Logic
Simulink-Maplesim-Labview
Matlab
Beacon
SCADE
Academia
DATA Verify
State-Space
Linear
System
Non-linearities
Modeline
Toolboxes
SISO
Matlab Tools
MIMO
Linear Analysis
Margin
Analysis
Theory
Verify
Shortcut
Simulink “Linearize”

## Slide 23: Linearization Example – deep dive
Drop the “delta” symbols to an implied “delta model”
And apply the initial conditions at the known stability points:

## Slide 24: Linearization Example
Consider a simple pendulum with applied torque t :
The equation of motion is:
Nonlinear Differential Equations
Physical System


t
q
M
l
b
Linear Differential Equations
The Linear Differential Equations at two natural stability points are:
Notes: You know by inspection that the system has two equilibrium points: and
The one at 0 is stable. The one at the top is unstable. The linearization process should reveal this.
You know by inspection that the system has two equilibrium points: 𝜃=0 and 𝜃=𝜋
The one at 0 is stable. The one at the top is unstable. The linearization process should reveal this.

## Slide 25: Exercise #1
Open Matlab R2013A or later
Enter the following at the command line:
  g = 32.2; % Gravity, ft/sec^2
  l = g*(1/(2*pi))^2; % Pendulum length for 1 sec period, ft
  b = 0.01; % Damping, lbf/(ft/sec)
  d = 1; % Diameter steel pendulum sphere, in
  M = 4/3*pi*(d/2)^3*.3/g; % Mass of ball, slugs
  Tpulse = 1; % Pulse time, sec
  Hpulse = 10; % Pulse height, ft-lbf
  Dpulse = 0.1; % Pulse duration, sec
Open a new Simulink diagram. Save it as “myPendulum.slx”
Open “ClassroomLibrary.” If no icons appear, then make sure the “SimulinkLibrary” folder is present and try again.
Draw the system using the blocks available in the Library
Connect the Impulse source and scope to the system. Run it. Save it. Is the observed natural period 1 second?

## Slide 26: Transfer Functions

## Slide 27: Progress – Model to Linear D.E.
Nonlinear Differential Equations
Linear Differential Equations
Transfer Function
Physical System



q
M
l
Notes: The goal is Transfer Functions

## Slide 28: An Aside: State Space
Recall Taylor Series Expansion of Partial Differential Equation
It is common to separate internal and external influences. This allows Eigenvalue analysis (states) separate from Boundary Value solutions.
Abbreviate
Notes: State Space is extremely useful as a bridge between different kinds of analysis tools.

## Slide 29: State Space Continued
Further generalize the internal states, x. Note that ANY state has a value and a derivative. The second derivative is the derivative of the state representing the first derivative, and so on:
Accompanying any dynamical system will be a set of O.D.E.s describing the equations of motion:

## Slide 30: State Space Continued
Now a general single-input, single-output (SISO) dynamical system will have a system of equations as it’s general representation.
Define some small letters to clean up the nomenclature:

## Slide 31: State Space Concluded
In general, all the parameters are vectors or arrays with all sorts of real-world cross-coupling and will be multi-input, multi-output (MIMO).

## Slide 32: This “State” Concept Can Be Leveraged to Create a Nice Block Diagram Connection. If this all seems a mish-mash it is. These are different symbols for representing the same concept. In fact, a Bode plot is another symbol.

## Slide 33: How it All Connects – these are all mathematically equivalent
ODE
Complex derivations
Math ‘engine’
Physically intuitive
MIMO shorthand
GUI Application
MIMO shorthand
GUI Application
Control Intuitive (Bode bridge)
DSP connection by Fourier

## Slide 34: Example: Derivation of Transfer Function from Block Diagram
These are all the clues you need to know.
Block diagrams are drawings of algebraic equations.

## Slide 35: Example Cont’d - Transfer Function
Consider a simple pendulum with applied torque t :
The equation of motion is:
Nonlinear Differential Equations
Physical System



Linear Differential Equations
A transfer function can now be derived:
Transfer Function
t
q
M
l
b
Linearize and apply at the bottom dead-center:

## Slide 36: Conclusion – Model to LTI
Nonlinear Differential Equations
Linear Differential Equations
Transfer Function
Physical System




State-Space
Block Diagram
t
q
M
l
b


Control Design
Notes: More on this later. Draw in Simulink now?

## Slide 37: In-Class Exercise:
Draw pendulum in Simulink
Generate time response; verify period of oscillation
Repeat in Matlab using SS. Use CL and functions to verify Simulink result
Repeat in Matlab using LTI.....Verify Eigenvalues. Make LTI steps and Bodes

## Slide 38: Frequency Response

## Slide 39: Types of Responses
Consider a typical second order system:
where n = 10 and  = 0.3
The following responses are presented on the next slide:
Unforced response (with initial condition)
Impulse response
Step response
Sinusoidal response
From now on we're going to concentrate on the sinusoidal or “frequency response.”

## Slide 40
Do all these examples in Simulink during class. Figure out a streamlined way to do it, e.g. interactive script that pages through

## Slide 41: The Frequency Response
What is it?
If a stable linear time invariant system is driven with a steady sinusoidal input, the output will be another sinusoid of the same frequency but with a different amplitude and phase shift.
The frequency response of the system relates the output sinusoid
amplitude and phase shift to that of the input:
H (LTI Sys)
In dynamic systems both the ratio B/A and the phase angle f are functions of the frequency w .

## Slide 42: What is Frequency Response (continued)
A Bode plot shows the complete picture of B/A and f :
Note that the frequency axis is a log scale, and the magnitude is measured in decibels. This allow the response to be estimated as a series of straight lines. Also note the shape:
This is typical of physical systems
Amplitude ratio rolls off as frequency increases
Phase angle is negative
They are often low pass—high frequencies are attenuated
They exhibit phase loss or phase lag

## Slide 43: What is Frequency Response (continued)
Let’s look at some sinusoidal responses of
Note that as frequency gets large the output cannot keep up:
Do all these examples in Simulink during class. Figure out a streamlined way to do it, e.g. interactive script that pages through

## Slide 44
Do all these examples in Simulink during class. Figure out a streamlined way to do it, e.g. interactive script that pages through

## Slide 45: What is Frequency Response (continued)
Resonant systems have a frequency range where the output is amplified
Consider sinusoidal responses shown on the next page for
Note the amplification at w = 10 which is at the natural frequency of the system:
where n = 10 and  = 0.3

## Slide 46
Do all these examples in Simulink during class. Figure out a streamlined way to do it, e.g. interactive script that pages through

## Slide 47: Backup