## Slide 1: Control of an Electrically Powered Two-Spool Turbine Device Advanced Courses in Engineering 19 Jan 2017 rev. 1
Former Instructors:
Dave Gutz (rev 2017-1)
PICTURE

## Slide 2: Outline
Description of Project
Wind Turbine Primer
Modeling and Linearization
Lab

## Slide 3: Description of Project

## Slide 4
Regulator: Subsystem or independent device that determines and maintains the operating parameters of a system, usually within certain prescribed or preset limits. Read more: http://www.businessdictionary.com/definition/regulator.html
In control theory, a controller is a device, historically using mechanical, hydraulic, pneumatic or electronic techniques often in combination, but more recently in the form of a microprocessor or computer, which monitors and physically alters the operating conditions of a given dynamical system.[1] [2]Typical applications of controllers are to hold settings for temperature, pressure, flow or speed.
Open-loop control can be used in systems sufficiently well-characterized as to predict what outputs will necessarily achieve the desired states. For example, the rotational velocity of an electric motor may be well enough characterized for the supplied voltage to make feedback unnecessary.
The drawback of open-loop control is that it requires perfect knowledge of the system (i.e. one knows exactly what inputs to give in order to get the desired output), and it assumes there are no disturbances to the system.

## Slide 5: Wind Turbine Primer

## Slide 6: Wind Turbine Overview

## Slide 7: Wind Turbine Primer
http://www.nrel.gov/docs/fy12osti/52780.pdf
Santoso,S. and Singh, M. “Dynamic Models for Wind Turbines and Wind Power Plants,” National Renewable Energy Laboratory Publication, UT Austin, Austin, Texas, NREL/SR-5500-52780 October, 2011.
https://en.wikipedia.org/wiki/Variable_speed_wind_turbine

## Slide 8: Power Coefficient Characterized by Tip Speed Ratio
https://en.wikipedia.org/wiki/Variable_speed_wind_turbine
Slope is related to damping torque ( N )

## Slide 9
Get content from my white book
Get Cp curves from my personal OneNote
Assumption: neglect laminar flow Re effects

## Slide 10: Deriving Damping from Measured Time Constant
, chain rule

## Slide 11: ESC – Electronic Speed Control of Brushless DC Motor (BLDC)

## Slide 12: DC Motor Dynamic Model
http://www.profjrwhite.com/system_dynamics/sdyn/s6/s6fmathm/s6fmathm.html
Bandwidth > 30 Hz

## Slide 13: Modeling

## Slide 14: Moment of Inertia of Propeller

## Slide 15: Motor Constants – SI Units Assumptions
The main thing I want you to take away from this post is that when a motor rotates it generates a back-emf. That back-emf is proportional to the motor speed and the Kv constant tells you how they relate to each othe

## Slide 16
2040 Brushless Inrunner Motor 4800kv

## Slide 17: Landscape of Control System Analysis
Physical System
Non-Linear Ordinary Differential Equations
Linear Differential Equations
Block Diagram
Control
Models
Z-Transform
Embedded
Logic
Simulink-Maplesim-Labview
Matlab
Beacon
SCADE
Academia
DATA Verify
State-Space
Linear
System
Non-linearities
Modeline
Toolboxes
SISO
Matlab Tools
MIMO
Linear Analysis
Margin
Analysis
Theory
Verify
Shortcut
Simulink “Linearize”

## Slide 18: Linearization
Consider a general nonlinear equation:
Suppose it has an equilibrium at (x0 , y0), linearize the equation about (x0 , y0) by expanding it into a Taylor series about x0:
Note that if x is close to x0 (equilibrium + small deflections):
Notes: Equilibrium at (x0 , y0)—this means if you initially configure the system at this point it won’t move
Note that if x is close to x0 then x – x0 is small and the higher order terms can be dropped

## Slide 19: Linearization (continued)
can be turned into a linear equation via a change of variables:
Where y = y – y0 and x = x – x0 . Note that
Linearized equations only valid close to equilibrium
Different equilibrium point means different linear equations
Notes: Taylor Series’ method can be generalization using the Chain Rule

## Slide 20: Linearization Example
Consider a simple pendulum with applied torque t :
The equation of motion is:
Nonlinear Differential Equations
Physical System


Linear Differential Equations
t
q
M
l
b
Notes: You know by inspection that the system has two equilibrium points: and
The one at 0 is stable. The one at the top is unstable. The linearization process should reveal this.
You know by inspection that the system has two equilibrium points: 𝜃=0 and 𝜃=𝜋
The one at 0 is stable. The one at the top is unstable. The linearization process should reveal this.

## Slide 21: Linearization Example – deep dive
Want to linearize
so we have
about

## Slide 22: Linearization Example – deep dive
Drop the “delta” symbols to an implied “delta model”
And apply the initial conditions at the known stability points:

## Slide 23: Linearization Example
Consider a simple pendulum with applied torque t :
The equation of motion is:
Nonlinear Differential Equations
Physical System


t
q
M
l
b
Linear Differential Equations
The Linear Differential Equations at two natural stability points are:
Notes: You know by inspection that the system has two equilibrium points: and
The one at 0 is stable. The one at the top is unstable. The linearization process should reveal this.
You know by inspection that the system has two equilibrium points: 𝜃=0 and 𝜃=𝜋
The one at 0 is stable. The one at the top is unstable. The linearization process should reveal this.

## Slide 24: Exercise #1
Open Matlab R2013A or later
Enter the following at the command line:
  g = 32.2; % Gravity, ft/sec^2
  l = g*(1/(2*pi))^2; % Pendulum length for 1 sec period, ft
  b = 0.01; % Damping, lbf/(ft/sec)
  d = 1; % Diameter steel pendulum sphere, in
  M = 4/3*pi*(d/2)^3*.3/g; % Mass of ball, slugs
  Tpulse = 1; % Pulse time, sec
  Hpulse = 10; % Pulse height, ft-lbf
  Dpulse = 0.1; % Pulse duration, sec
Open a new Simulink diagram. Save it as “myPendulum.slx”
Open “ClassroomLibrary.” If no icons appear, then make sure the “SimulinkLibrary” folder is present and try again.
Draw the system using the blocks available in the Library
Connect the Impulse source and scope to the system. Run it. Save it. Is the observed natural period 1 second?

## Slide 25: Transfer Functions

## Slide 26: Progress – Model to Linear D.E.
Nonlinear Differential Equations
Linear Differential Equations
Transfer Function
Physical System



q
M
l
Notes: The goal is Transfer Functions

## Slide 27: An Aside: State Space
Recall Taylor Series Expansion of Partial Differential Equation
It is common to separate internal and external influences. This allows Eigenvalue analysis (states) separate from Boundary Value solutions.
Abbreviate
Notes: State Space is extremely useful as a bridge between different kinds of analysis tools.

## Slide 28: State Space Continued
Further generalize the internal states, x. Note that ANY state has a value and a derivative. The second derivative is the derivative of the state representing the first derivative, and so on:
Accompanying any dynamical system will be a set of O.D.E.s describing the equations of motion:

## Slide 29: State Space Continued
Now a general single-input, single-output (SISO) dynamical system will have a system of equations as it’s general representation.
Define some small letters to clean up the nomenclature:

## Slide 30: State Space Concluded
In general, all the parameters are vectors or arrays with all sorts of real-world cross-coupling and will be multi-input, multi-output (MIMO).

## Slide 31: This “State” Concept Can Be Leveraged to Create a Nice Block Diagram Connection. If this all seems a mish-mash it is. These are different symbols for representing the same concept. In fact, a Bode plot is another symbol.

## Slide 32: How it All Connects – these are all mathematically equivalent
ODE
Complex derivations
Math ‘engine’
Physically intuitive
MIMO shorthand
GUI Application
MIMO shorthand
GUI Application
Control Intuitive (Bode bridge)
DSP connection by Fourier

## Slide 33: Example: Derivation of Transfer Function from Block Diagram
These are all the clues you need to know.
Block diagrams are drawings of algebraic equations.

## Slide 34: Example Cont’d - Transfer Function
Consider a simple pendulum with applied torque t :
The equation of motion is:
Nonlinear Differential Equations
Physical System



Linear Differential Equations
A transfer function can now be derived:
Transfer Function
t
q
M
l
b
Linearize and apply at the bottom dead-center:

## Slide 35: Conclusion – Model to LTI
Nonlinear Differential Equations
Linear Differential Equations
Transfer Function
Physical System




State-Space
Block Diagram
t
q
M
l
b


Control Design
Notes: More on this later. Draw in Simulink now?

## Slide 36: In-Class Exercise:
Draw pendulum in Simulink
Generate time response; verify period of oscillation
Repeat in Matlab using SS. Use CL and functions to verify Simulink result
Repeat in Matlab using LTI.....Verify Eigenvalues. Make LTI steps and Bodes

## Slide 37: Frequency Response

## Slide 38: Types of Responses
Consider a typical second order system:
where n = 10 and  = 0.3
The following responses are presented on the next slide:
Unforced response (with initial condition)
Impulse response
Step response
Sinusoidal response
From now on we're going to concentrate on the sinusoidal or “frequency response.”

## Slide 39
Do all these examples in Simulink during class. Figure out a streamlined way to do it, e.g. interactive script that pages through

## Slide 40: The Frequency Response
What is it?
If a stable linear time invariant system is driven with a steady sinusoidal input, the output will be another sinusoid of the same frequency but with a different amplitude and phase shift.
The frequency response of the system relates the output sinusoid
amplitude and phase shift to that of the input:
H (LTI Sys)
In dynamic systems both the ratio B/A and the phase angle f are functions of the frequency w .

## Slide 41: What is Frequency Response (continued)
A Bode plot shows the complete picture of B/A and f :
Note that the frequency axis is a log scale, and the magnitude is measured in decibels. This allow the response to be estimated as a series of straight lines. Also note the shape:
This is typical of physical systems
Amplitude ratio rolls off as frequency increases
Phase angle is negative
They are often low pass—high frequencies are attenuated
They exhibit phase loss or phase lag

## Slide 42: What is Frequency Response (continued)
Let’s look at some sinusoidal responses of
Note that as frequency gets large the output cannot keep up:
Do all these examples in Simulink during class. Figure out a streamlined way to do it, e.g. interactive script that pages through

## Slide 43
Do all these examples in Simulink during class. Figure out a streamlined way to do it, e.g. interactive script that pages through

## Slide 44: What is Frequency Response (continued)
Resonant systems have a frequency range where the output is amplified
Consider sinusoidal responses shown on the next page for
Note the amplification at w = 10 which is at the natural frequency of the system:
where n = 10 and  = 0.3

## Slide 45
Do all these examples in Simulink during class. Figure out a streamlined way to do it, e.g. interactive script that pages through

## Slide 46: Integrator Frequency Response
Compute B/A and f analytically:

## Slide 47: Lag Frequency Response
Compute B/A and f analytically by figuring out the response to a sine wave:
Laplace transform of A sin(w t) (for t>0) is
So the output Laplace transform is
Expanding partial fractions yields:
output sinusoid
transient (goes away)
So by figuring out a formula for A1 you could at least get the magnitude response… COULD THERE BE A BETTER WAY???

## Slide 48: Lag Frequency Response (continued)
So… A better way to compute the lag frequency response involves looking at the transfer function in terms of the Fourier transform.
Let’s limit the Laplace variable s to just the imaginary axis, so s = jw
Note that H(jw) is a complex number that can be represented by a magnitude and a phase angle:

## Slide 49: Lag Frequency Response (continued)
So let’s compute m(w) and f(w) :

## Slide 50: Excel Frequency Response Example
Use complex number functions:
  COMPLEX(sigma, beta)
  IMSUM(<complex>,<complex>,…)
  IMPRODUCT(<complex>, <complex>,..)
  Mag = IMABS(<complex>)
  Phase = IMARGUMENT(<complex>)*180/PI()
Second order system gain=1/ IMABS(COMPLEX( 1-w^2/wn^2, 2*z*w/wn))
  Phase= -IMARGUMENT(COMPLEX( ))*180/PI()

## Slide 51: MATLAB Frequency Response Example
MATLAB is object-oriented. It knows what you’re trying to do.
Use SYSTEM functions:
  <tfPoly> = [a b c d];
  <sysTF> = tf(<numPoly>, <denPoly>)
  <sysSS> = ss(<sysTF>)
  <sysTF> = tf(<sysSS>)
  <OLTF> = G*H
  <CLTF> = G/(1+GH)
  Figure; step(<CLTF>)
  Figure; bode(<OLTF>)
Second Order example
  num = 1
  den = [1/wn^2 2*z/wn 1]
  sys2 = tf(num, den)
  sys2SS = ss(sys2)

## Slide 52: Lag Frequency Response (continued)
For a pure sinusoid input with amplitude 1 and zero phase, the magnitude and angle of H(jw) can be used to directly compute B/A and f that we originally wanted:
Since Bode plots use decibels:
Do all these examples in Simulink during class. Figure out a streamlined way to do it, e.g. interactive script that pages through

## Slide 53
Do all these examples in Simulink during class. Figure out a streamlined way to do it, e.g. interactive script that pages through

## Slide 54: Lead/Lag Frequency Response
Results for two cases:
Do all these examples in Simulink during class. Figure out a streamlined way to do it, e.g. interactive script that pages through

## Slide 55
Do all these examples in Simulink during class. Figure out a streamlined way to do it, e.g. interactive script that pages through

## Slide 56
Do all these examples in Simulink during class. Figure out a streamlined way to do it, e.g. interactive script that pages through

## Slide 59: Second Order Frequency Response
Frequency response shape depends heavily on value of z

## Slide 60
Do all these examples in Simulink during class. Figure out a streamlined way to do it, e.g. interactive script that pages through

## Slide 61: Pure Delay Frequency Response
Pure delay has no impact on gain but phase loss goes to infinity at high frequencies.
Sampled data systems appear to have output delayed by half the sample rate.
Do all these examples in Simulink during class. Figure out a streamlined way to do it, e.g. interactive script that pages through

## Slide 62: Frequency Responses are Additive
This is because logs of magnitudes (and phases) add when you multiply complex numbers together. Very convenient…
Do all these examples in Simulink during class. Figure out a streamlined way to do it, e.g. interactive script that pages through

## Slide 63: Closed Loop Transfer Function

## Slide 64: Loop Transfer Function/Closed Loop Transfer Function
Need to be aware of two definitions
G(s)
K(s)
+
-
H(s)
The Loop Transfer Function is the transfer function you get if you break the feedback loop at the last possible point; in the above diagram it’s the TF from e(t) to x(t):
The Closed Loop Transfer Function is just the transfer function from r(t) to y(t):
Note that the CLTF tends to be more complex than the loop transfer function, parameters from controller more tangled up.

## Slide 65: Using the Open Loop TF to Infer CLTF Poles
Recall that the CLTF poles always satisfy:
Crudely put*, when the open loop transfer function reaches or exceed the condition of -1 (180 degrees at 0 dB) the system becomes unstable.
  Intuitively this means that the control action large enough to amplify (re-enforce) an out of phase response
Where Gl(s) is the loop TF
Notes: *Technically, when the open loop transfer function encircles the -1 point on a Nyquist diagram of phase versus magnitude.

## Slide 66: Gain and Phase Margin on Bode Plot
Margins best visualized on Bode plot of open loop transfer function
If either margin is zero or negative, system is unstable. This is this lecture’s definition of instability.
REMEMBER: THIS IS THE OPEN LOOP TRANSFER FUNCTION
Gain Margin
Phase Margin
Magnitude
Phase
0 dB
-90
-180
Gain Crossover (“the crossover”)
Phase Crossover
Notes: Phase Margin is the difference in phase between Gl(jw) and –180 degrees when the magnitude of Gl(jw) is 1 (0 dB)
Gain Margin is the difference between the magnitude of Gl(jw) and 1 (0 dB) when phase is –180 degrees (how much would we need to multiply Gl(jw) to get 1)
Consider a real world control:
Gain of open loop system is the product of the compensator gain and the plant gain. We know the compensator gain (we designed it, but the plant gain comes from a model.
So gain margin tells is how much the actual plant gain can be different from our model without causing instability
Gain margin requirement for a control design is chosen based on our confidence in our model
  E.g. for an engine how well do we know  Qu / wf ?
  Typical choice is 6dB (a factor of two)
Phase margin tells us the same thing for model uncertainty in dynamics and delays

## Slide 67: Relationships Between Open and Closed Loop Frequency Responses and Time Response
Open Loop Frequency Response Characteristics:
  Gain Crossover (where gain crosses 0 dB)
  *Phase Crossover (where phase crosses –180 deg)
  Gain Margin
  *Gain Rolloff Margin
  Phase Margin
  *Delay margin (number of delays at sample rate to destabilize)
Closed Loop Frequency Response Characteristics:
  Gain Bandwidth (where gain hits –3 dB) not crossover
  Phase Bandwidth (where phase hits –45 deg) not crossover
  Peaking – caused by “near” instability e.g. low margins
Time Response Characteristics:
  Rise time
  Settling time
  Overshoot
Other Characteristics:
  Pole location (for real poles)
  Natural Frequency and Damping (for complex poles)
Notes: *Seldom used

## Slide 68: Relationships Between Open and Closed Loop Frequency Responses and Time Response (continued)
Have already seen these relationships:
  High bandwidth  Fast rise time High natural frequency High pole location
  High peaking  Faster rise time High overshoot Slow settling time Low damping
Now we can add the open loop relationships:
  High gain crossover  High bandwidth
  High phase margin  Low peaking High damping
In fact, for second order systems:

## Slide 69: Control Design

## Slide 70: Control Design Objectives
Objectives of control design are twofold:
  Performance
    Rise and settling time
    Overshoot
    Bandwidth  crossover
  Robustness
    Gain margin
    Phase margin
To achieve robustness objectives need to shape open loop frequency response
Since open loop crossover relates to performance it is convenient to use open loop frequency response as vehicle for control design
Typical design objectives…
  Target phase margin of 55 degrees
  Target crossover of 3 rad/sec
  Min gain margin of 6 dB
Notes: There are no DP requirements in 2014 for gain margin and phase margin.

## Slide 71: Lead Compensation Example
Consider an uncompensated plant:
Too slow (crossover too low)
Negative phase margin at target crossover
Step 1: Choose unity gain lead/lag compensator to build needed phase at target crossover
Notes: Lead adds phase and gain  lower loop gain to re-establish crossover frequency.

## Slide 72: Lead Compensation Example (continued)
Combine unity gain compensator with plant (linear superposition applies here)
Note that compensator does indeed boost the phase such that phase margin is now acceptable. What about gain bandwidth?

## Slide 73: Lead Compensation Example (continued)
Step 2: Choose compensator gain to hit target crossover
So now our combined compensator and plant has the desired crossover and phase margin.
Now we can go look at the closed-loop frequency response and time response to verify the design.

## Slide 74: Lead Compensation Example (continued)
Final Note: By designing the lead compensator we have hit both performance and robustness objectives
wc  bandwidth  rise time
PM  stability  low overshoot

## Slide 75: Notional Ideal Control System
The most desirable dynamic behavior: first order lag
Do these cancel?
Why not or why?
Notes: Infinite gain margin
90 degrees phase margin
Simply raise the gain as much as can be tolerated/supported by the hardware
The cancellation activity raises the power level inside the loop potentially reaching hardware limits at low gains.
Still a worthy notion

## Slide 76: Control Design Example Summary

## Slide 77: Frequency Domain Control Design Example Summary
Let’s use what you’ve learned to review the process for example #2
Implement Model
Control
Design
Nonlinear Differential Equations
Linear Differential Equations
Transfer Function
Physical System



-Requirements
-Trade studies


Verify
Model

-Another model
-Test
Iterate as needed

Control Design
Notes: Block Diagram  Derive plant time constant
Matlab LTI Systems
  Linear analysis
    Architecture
    Stability margins
    Control response optimization
Simulink
  Non-linear simulation
  Linear model generation
  Verification
  Drive with test data
  Shareable with customers/suppliers
  Structure standardization
Matlab command line (“cli”)
  Automation/scripting
  All Matlab commands and gui’s have a cli
Matlab State-space
  Eigenvalue analysis; modal analysis
Various Matlab Tools
  Automated tuning
  Method repository

## Slide 78: Example Conclusion – Close the Loop!
Nonlinear Differential Equations
Linear Differential Equations
Transfer Function
Physical System



t
q
M
l
b
b1
b2
b3
b4
b5
Frequency Response
(sisotool)

State-Space
Block Diagram


open
closed
Root Locus

Control
Design

## Slide 79: Rigid Pendulum Closed Loop Controller System Block Diagram
Strategy 1: Use Matlab’s built-in LQG tool
Plant poles at +/-5.65 r/s
Control
Design
Added the assumption that the pendulum is rigid

## Slide 80: Result Using sisotool for Air/Water Damping, Optimal Design Compensator
Gain Margin = 13.5 dB, 53.8 r/s (8.5 Hz)
Phase Margin = 44.4 deg, 17.2 r/s (2.7 Hz)
Settles to 95% in ~4sec
Automatic tuning seeks zero to cancel;
Fast poles to “carry” the leads”
Gain=0.587
Zeros at 5.6, 1.5 r/s
Poles at 0, 0, -42+/-42j
Trade study
Control
Design
Notes: Open R2013A or later.
% Bode design of regularPendulum
open('regularPendulum.mdl')
% This will automatically generate some Bode plots for reference and make assignments for later use:
sim('regularPendulum.mdl')
%
% scope will show all possible systems’ time responses
%%%%%%%%%%%%%%Command Line Basics%%%%%%%%%%%%
generated by File-Model Properties – Callbacks – InitFcn
LTI_Direct = SS = ABCD = LTI_Alg
%%%%%%%%%%%%%% Tools%%%%%%%%%%%%%%%
% Examine plant:
Analysis – Control Design – Linear Analysis – Exact Linearization - <pencil, pick i/o> - new Bode
Rename linsys1 to “plant”. Drag to MATLAB: workspace
Eig(plant)
0+/-5.6545i
% SisoTool start from command line
sisotool
Architecture – System Data – G=SS, H=1, C=Controller, F=1 (generated by File-Model Properties – Callbacks – PreLoadFcn)
% Can move zeroes and poles on lrc plot
% Used Automated Tuning – LQG Synthesis – default settings – 3rd order
% Linear Analysis
Analysis – Control Design – Linear Analysis Tool
Select ContComp as Open-loop Input and LTI Direct as Output Measurement
Rename system to ‘linsysLTI_Direct’ and drag to MATLAB workspace
figure(1); hold; bode(linsysLTI_Direct) % SAME!!
Select Sum1 as open-loop Input and Integrator2 as Output Measurement
Run new Bode and right-click – Characteristics – Margins to show gain margin and phase margin
% alternatively
Figure; bode(OLTF);

## Slide 81: Canceller Study
Notice that we’re using physical reasoning to design a controller
Control
Design
Strategy 2: Next try cancelling the plant (the best we can) and maximize K for best closed loop
Notes: % Use Matlab R2013a or later
open('regularPendulumCancel.mdl')
% This will automatically generate some Bode plots for reference and make assignments for later use:
sim('regularPendulumCancel.mdl')
tf(plant)
From input "torque, ft-lbf" to output "theta-rad":
205
------------------------
s^2 + 6.038e-05 s + 32.2
tf(Canceller)
s^2 + 6.038e-05 s + 32.2
--------------------------
0.0631 s^2 + 5.035 s + 205
% Analysis – Control Design – Linear Analysis
Alternate various i/o to create the “compensator plot”

## Slide 82: Redo Linear Design with Reduced Order Controller (canceller)
Gain Margin = inf
Phase Margin = 141 deg
Settles in ~1.8sec (3x improvement)
Some noise evident! Cancellation artifacts.
Gain=3.1 (HIGH!!)
1st order Compensator ‘unloaded’ by Canceller
Control
Design
Notes: % Use Matlab R2013a or later
open('regularPendulumCancel.mdl')
% This will automatically generate some Bode plots for reference and make assignments for later use:
sim('regularPendulumCancel.mdl')
tf(plant)
From input "torque, ft-lbf" to output "theta-rad":
205
------------------------
s^2 + 6.038e-05 s + 32.2
tf(Canceller)
s^2 + 6.038e-05 s + 32.2
--------------------------
0.0631 s^2 + 5.035 s + 205
% SisoTool start from command line
sisotool
Architecture – System Data – G=Canceller*SS, H=1, C=Controller, F=1 (generated by File-Model Properties – Callbacks – PreLoadFcn)
% Can move zeroes and poles on lrc plot
% Used Automated Tuning – LQG Synthesis – default settings –1st order

## Slide 83: Cautions – Which do you prefer? Which do you need?
Aggressive cancellation: control signal large. Power larger. Noisier.
Susceptible to variation – especially 2nd order. (Not really a problem for first order compensation)
Control
Design
125 ft-lbf peak
1.25 ft-lbf peak

## Slide 84: Let’s Talk about Damping – Making it Simple
A very common, very illustrative situation is square law load.
Hydraulic resistance, windage torque of all kinds…
One step up from linear…the first H.O.T.
Look how simple and high level. If know op condition know damping.
Notes: Operating point is 0 velocity

## Slide 85: Let’s Talk About Gain Scheduling (for Homework)
At GE Aviation “gain scheduling” governors
Method of “looking up” the appropriate gains and time constants in “lookup tables”
Operating condition changes slower than the dynamics of the loop to prevent interactions
Infinite variety of operating condition schedules. Try to trend these using dimensional analysis.

## Slide 86: Conclusion

## Slide 87: Review vs Rool Locus: Poles and Impulse Responses Connect
Real
Imaginary








stable exponential
unstable exponential
undamped sinusoid
damped sinusoid
unstable sinusoid

## Slide 88: Conclusion
If you don’t have a linear system you can always make one
  Linearization turn-the-crank process
  We do it because we can!
All linear systems have a frequency response
  Sinusoids pass through linear systems without changing their frequencies, only amplitude and phase
  Easy to compute from Laplace Transform - just replace s with jw
Frequency response can be used as a powerful design tool
  Can use open-loop response to shape closed loop
  Phase and gain margin can guarantee the system will work even if you screwed up the modeling
Nonlinear Differential Equations
Linear Differential Equations
Transfer Function
Physical System




State-Space
Block Diagram


Control
Models
Verify
Model
Iterate as needed

Control
Linear
Analysis
Ordinary Differential Equations
Partial Differential Equations
Simulink
Matlab
Beacon
SCADE
Academia
Z-Transform
Laplace
Transform

## Slide 89
If you decide to pursue this topic further:
Constructing a square wave with sine waves…Fourier and DSP, Sampling Theory, Digital Control

## Slide 90: Backup

## Slide 91: Linearization Example 1
Consider the differential equation
This equation has two equilibrium points (+/- 2):

## Slide 92: Linearization Example 1 (continued)
Linearizing dy/dt = 3y2 – 12 about y0 = 2 yields
Lazy individuals have been known to drop the D and just write that last expression as
With the understanding that y is now a reference to the equilibrium about which the equation was linearized. DO NOT FORGET THIS!!

## Slide 93: Linearization Example 1 (continued)
Linearizing dy/dt = 3y2 – 12 about y0 = –2 yields
Note that the linearized equation is different from before—there's now a minus sign in front of the 12. The solution for this equation is
Whereas the solution for y0 = 2 is

## Slide 94
Thus if the system is perturbed from the first equilibrium point it will diverge from this point (the point is unstable).
If it is perturbed from the second equilibrium it will return (the equilibrium is stable). Similar to a ball on hill and/or valley.

## Slide 95: Sensitivity Trade Study of Pendulum Controller
Look at damping variation
Retune for variation
Reexamine performance for net effect
Back to Lecture

## Slide 96: Add Heavy Damping, Design Compensator
Gain Margin = inf
Phase Margin = 7.0 deg, 1090 r/s (173 Hz)
Gain=0.587
Zeros at 5.6, 1.5 r/s
Poles at 0,0, -42+/-42j
Damping destablized! Counter-intuitive
Back to Lecture
Notes: open('regularPendulum.mdl')
% This will automatically generate some Bode plots for reference and make assignments for later use:
swHeavy = 1;
sim('regularPendulum.mdl')
tf(Controller)
248.6 s^2 + 1747 s + 2031
-------------------------
s^3 + 83.04 s^2 + 3460 s

## Slide 97: Add Heavy Damping, Re-Optimized Design Compensator
Gain Margin = 13.5 dB, 53.8 r/s (8.5 Hz)
Phase Margin = 44.4 deg, 17.2 r/s (2.7 Hz)
Gain 0.595
Zeros at 5.9, 1.4 r/s
Poles at 0,0, -42+/-42j
Slight retuning re-stabilized!
Back to Lecture
Notes: open('regularPendulum.mdl')
% This will automatically generate some Bode plots for reference and make assignments for later use:
swHeavy = 1;swHeavyComp=1;
sim('regularPendulum.mdl')
tf(Controller)
245 s^2 + 1791 s + 2059
------------------------
s^3 + 83.04 s^2 + 3460 s
roots(cnum)
ans =
-5.8824
-1.4286
roots(cden)
ans =
0.0000 + 0.0000i
-41.5225 +41.6664i
-41.5225 -41.6664i

## Slide 98: Re-examine Nominal Air Damping, Heavy Design Compensator
Gain 0.595
Zeros at 5.9, 1.4 r/s
Poles at 0,0, -42+/-42j
Gain Margin = 13.4 dB, 53.4 r/s (8.5 Hz)
Phase Margin = 42.1 deg, 17.2 r/s (2.7 Hz)
Net effect: damping destablized but not much!
Back to Lecture
Notes: open('regularPendulum.mdl')
% This will automatically generate some Bode plots for reference and make assignments for later use:
swHeavy = 0;swHeavyComp=1;
sim('regularPendulum.mdl')

## Slide 99: Poles and Zeros
What do they mean? Why do we care about them?
Consider a transfer function H(s) which represents the impulse response of an LTI system. Recall that we can always write H(s) as a partial fraction expansion:
The pi’s are the poles. Each pole is either real or complex and either unique or repeated
Recall that we can return each term individually to the time domain:

## Slide 100: An Aside: The Fourier Transform
You can get the Fourier Transform of a signal by taking the Laplace transform and replacing s with jw
Recall from math class: You can always take a periodic signal and represent it as an infinite sum of discrete sinusoids. This is called a Fourier Series.
  First sinusoid frequency is same as signal, then 2x that of signal, 3x, etc.
If you have a signal that is not periodic you can still represent it with sinusoids but the frequencies are infinitely close together
Fourier Transform represents the coefficients of the sinusoids that make up a signal (impulse response if it’s a transfer function)
  It is a complex number that’s a function of w .
  Magnitude of the complex number is the amplitude of the sinusoid, angle is the phase offset

## Slide 101: An Aside: The Fourier Transform (continued)
Convolution of two sinusoids:
  Amplitudes multiply, phases add
Since we’re interested in the response of the system to a unit sinusoid with zero phase offset, we need only look at the Fourier Transform at that frequency
Another way to look at it: The Fourier transform of the impulse is 1 (at all frequencies). Thus the Fourier transform of the impulse response gives us the response to unit sinusoids at all frequencies.
Why the heck do we use Laplace transforms if Fourier Transforms are so useful (convolution works, etc)?
Laplace transform is really a generalization of the Fourier transform, works for unstable exponentials (Fourier does not— see integral above)

## Slide 102: Relationship between Poles/Step Response and Frequency Response
Since a step is made up of all odd harmonics (see next slide), the higher the frequency that can pass through a system without attenuating the better the step response.
System bandwidth is a measure of how high a frequency can pass through a system without attenuation—typically chosen at -3dB attenuation but for a digital system the -45 degree phase loss is more appropriate due to phase losses added by sampling delays
The next plots compare frequency responses with step responses.

## Slide 103: Plotting a Frequency Response on the s-Plane
Just as you can plot magnitude and phase as a function of frequency, you can plot the frequency response on the s-plane
Imaginary
Real

## Slide 104: Shaping Open Loop Frequency Response
Two primary methods for this class
  Lead compensation
  Lag compensation
Numerous advanced methods (mostly for MIMO systems)
  Model Matching
  H2
  H
   synthesis